## Slide 1
Status of EIC Calorimeter R&D
at BNL
EIC Detector R&D Committee Meeting
July 21, 2014
S.Boose, A. Franz, J.Haggerty, E.Kistenev, E,Mannel, S.Stoll, A.Sickles, C.Woody
PHENIX Group
E.Aschenauer, A.Kiselev
SPIN and EIC Group

## Slide 2: Test of Tilted Plate Tungsten SciFi EMCAL
Prototype completed in January 2014
Tested at Fermilab in February of 2014 along with PHENIX HCAL
First test of this new calorimeter configuration

## Slide 3
Fermilab Beam Test
Test of combined EMCAL and HCAL prototypes at Fermilab in Feb 2014
(sPHENIX 2/5-2/25, STAR 2/26-3/18)
sPHENIX
HCAL
sPHENIX
EMCAL

## Slide 4
MT6 Test Beam Area
Location of both calorimeters
Both calorimeters were placed at the far downstream end of the test beam line due to rigging requirements for the HCAL
Resulted in having much material in front of the EMCAL even after removing many other detectors in the beamline

## Slide 5
Fermilab Beam Test

## Slide 6: Measurement of Light Output
Light yield ~ 100 p.e. on PMT
Energy deposit = 29 MeV
- total energy deposit from mip traversing perpendicular (12 layers) of one tower of absorber stack
    3.5 p.e./MeV
    3500 p.e./GeV
Assume 90% light collection
  3900 p.e./GeV in calorimeter
Light collection efficiency of 4.7% from cavities  ~ 180 p.e./GeV with SiPM (assuming PDESiPM  QEPMT)
 ~ 7% contribution to energy
resolution from photon statistics
PMT coupled directly onto one tower module of absorber stack (12 layers)
Beam (120 GeV p) traverses tower perpendicular to plates (Edep = 29 MeV)
Light yield measured in three positions across tower module

## Slide 7: Tower Readout with SiPMs
Test with 3 central rows of towers with 2 SiPM readout
2 SiPMs
1 SiPM
x2
Using 2 SiPMs effectively doubles the light output as expected

## Slide 8: Transverse Position Dependence
8 GeV electrons
Sum of a Single Row of Towers
Sum of 3 Rows of Towers
~ 5%
~ 5% variation across a tower

## Slide 9: Longitudinal Position Dependence
5 different calorimeter positions along fiber direction
120 GeV protons
~ 2%
~ 2% variation along length
Dy = 23 mm
Scan along calorimeter with beam
Scan along fibers with source

## Slide 10: Linearity
electrons

## Slide 11: Energy Resolution
90°
10°
20°
Expected Resolution:
Sampling: ~ 15% /√E
Photostatistics: ~ 7.5%/√E
Constant (nonuniformities) ~ 5%
Combined: ~ 17%/√E  5%
Measured Resolution: ~ 22%/√E  10%
Difference most likely due to lack of calibration for temperature drift of SiPMs

## Slide 12: Conclusions and Future Plans
First test of the tilted plate tungsten SciFi EMCAL was competed at Fermilab in February 2014
Performance in many respects was quite good (uniformity of response across towers, longitudinal uniformity, light output, linearity). Light output can easily be increased by increasing number of SiPMs.
Energy resolution was not as expected, most likely due to lack of control over calibration due to temperature variation of SiPMs.
Given the very promising results with the SPACAL, we will not pursue the tilted plate or accordion design any further at this time and will consolidate our efforts to develop the SPACAL
Will continue to develop our front end electronics and readout system but will tailor it more to the SPACAL design

## Slide 13: Budget for Future R&D